## Slide 1: STM32 Dist.
Micro201

## Slide 2: 5. BSP package
FMC SDRAM BSP lab (5.1)
LCD BSP Print text lab (5.2)
I2C BSP EEPROM lab (5.3)
SPI BSP GYROSCOPE lab (5.4)
5

## Slide 3: 5.1 BSP SDRAM lab

## Slide 4: Use BSP for SDRAM initialization
Create project in CubeMX
  Menu > File > New Project
  Select STM32F4 > STM32F429/439 > LQFP144 > STM32F439ZITx
We need only blank project with clock initialization
  We only set the RCC and configure the core to maximum speed
5.1

## Slide 5: Use BSP for SDRAM initialization
Now we have bank project
For SDRAM we need to include more parts
Our project
Discovery drivers
HAL API
Components
stm32f4xx_discovery.c
stm32f4xx_discovery_sdram.c
stm32f4xx_discovery_io.c
ili9341.c
lis3dsh.c
stmpe811.c
stm32f4xx_II_fmc.c
stm32f4xx_hal_sdram.c
BSP package
stm32f4xx_hal_spi.c
stm32f4xx_hal_i2c.c
stm32f4xx_hal.c
5.1

## Slide 6: Use BSP for SDRAM initialization
BSP SDRAM organization
Our project
Discovery drivers
HAL API
Components
stm32f4xx_discovery.c
stm32f4xx_discovery_sdram.c
stm32f4xx_discovery_io.c
ili9341.c
lis3dsh.c
stmpe811.c
stm32f4xx_II_fmc.c
stm32f4xx_hal_sdram.c
BSP package
stm32f4xx_hal_spi.c
stm32f4xx_hal_i2c.c
stm32f4xx_hal.c
5.1

## Slide 7: Use BSP for SDRAM initialization
BSP SDRAM organization
Our project
Discovery drivers
HAL API
Components
stm32f4xx_discovery.c
stm32f4xx_discovery_sdram.c
stm32f4xx_discovery_io.c
ili9341.c
lis3dsh.c
stmpe811.c
stm32f4xx_II_fmc.c
stm32f4xx_hal_sdram.c
BSP package
stm32f4xx_hal_spi.c
stm32f4xx_hal_i2c.c
stm32f4xx_hal.c
2. include stm32f4xx_discovery.h
1. include stm32f4xx_discovery_sdram.h
5.1

## Slide 8: Use BSP for SDRAM initialization
BSP SDRAM organization
Our project
Discovery drivers
HAL API
Components
stm32f4xx_discovery.c
stm32f4xx_discovery_sdram.c
stm32f4xx_discovery_io.c
ili9341.c
lis3dsh.c
stmpe811.c
stm32f4xx_II_fmc.c
stm32f4xx_hal_sdram.c
BSP package
stm32f4xx_hal_spi.c
stm32f4xx_hal_i2c.c
3. include stm32f4xx_hal.h
stm32f4xx_hal.c
4. stm32f4xx_hal.h include all peripherals which are used in stm32f4xx_discovery.c
5.1

## Slide 9: Use BSP for SDRAM initialization
BSP SDRAM organization
Our project
Discovery drivers
HAL API
Components
stm32f4xx_discovery.c
stm32f4xx_discovery_sdram.c
stm32f4xx_discovery_io.c
ili9341.c
lis3dsh.c
stmpe811.c
stm32f4xx_II_fmc.c
stm32f4xx_hal_sdram.c
BSP package
stm32f4xx_hal_spi.c
stm32f4xx_hal_i2c.c
stm32f4xx_hal.c
5. stm32f4xx_hal.h include all peripherals which are used in stm32f4xx_discovery_sdram.c
5.1

## Slide 10: Use BSP for SDRAM initialization
BSP SDRAM organization
Our project
Discovery drivers
HAL API
Components
stm32f4xx_discovery.c
stm32f4xx_discovery_sdram.c
stm32f4xx_discovery_io.c
ili9341.c
lis3dsh.c
stmpe811.c
stm32f4xx_II_fmc.c
stm32f4xx_hal_sdram.c
BSP package
stm32f4xx_hal_spi.c
stm32f4xx_hal_i2c.c
stm32f4xx_hal.c
6. HAL_SDRAM_Init is function from stm32f4xx_discovery_sdram.c
7. HAL_SDRAM_Init
call functions from stm32f4xx_II_fmc.c
8. stm32f4xx_II_fmc.c use functions from stm32f4xx_hal_sdram.c
5.1

## Slide 11: Use BSP for SDRAM initialization
stm32f4xx_hal_ppp.h
stm32f4xx_hal_ppp_ex.h
stm32f4xx_hal.h
stm32f4xx_it.c
user_code.c
Source files
Include files
stm32f4xx_hal_def.h
stm32f4xx_hal_conf.h
stm32f4xx_hal_ppp.c
stm32f4xx_hal_ppp_ex.c
stm32f4xx_hal.c
HAL Drivers
User Code
user_code.h
stm32f4xx_it.h
BSP Drivers
Stm32f4xx_discovery.c
Stm32ffxx_discovery_sdram.c
Stm32f4xx_discovery.h
Stm32ffxx_discovery_sdram.h
5.1

## Slide 12: Use BSP for SDRAM initialization
The copy part
  In our project in Drivers folder create folder BSP
  Now go into CubeMX repository …\STM32Cube_FW_F4_V1.3.0\Drivers\BSP\
  And copy Components and STM32F429I-Discovery into BSP folder
Copy folders into BSP
5.1

## Slide 13: Use BSP for SDRAM initialization
Now we need to add this files also in project
  Create BSP folder in project
  Right click on project in Workplace>ADD>Group
  Name it BSP
  Now right click on BSP>ADD>Files
  From Drivers\BSP\STM32F429I-Discovery\ add stm32f429i_discovery.c and stm32f429i_discovery_sdram.c
5.1

## Slide 14: Use BSP for SDRAM initialization
The stm32f429i_discovery.c contains functions for all components on discovery kit (LCD, GYRO,…)
Then we also need add into project HAL library which handle their interface (I2C, SPI, … )
Right click on STM32F4xx_HAL_Drive>ADD from \Drivers\STM32F4xx_HAL_Driver\Src
  stm32f4xx_hal_i2c.c
  stm32f4xx_hal_spi.c
  stm32f4xx_hal_sdram.c
  stm32f4xx_II_fmc.c
5.1

## Slide 15: Use BSP for SDRAM initialization
Now add the include paths for this new files
  Right click on project>Options>Category C/C++Compiler>Preprocesor
  Into Defined symbols add USE_STM32F429I_DISCO
  This allow use BSP functions
  Into additional includes add $PROJ_DIR$\..\..\Drivers\BSP\STM32F429I-Discovery
  Button OK
  Button OK close project options
5.1

## Slide 16: Use BSP for SDRAM initialization
Now last thing is allow to include new HAL files which we added
  Open stm32f4xx_hal_conf.h in ..\Inc\
  Uncomment files which we added
  HAL_SDRAM_MODULE_ENABLED
  HAL_I2C_MODULE_ENABLED
  HAL_SPI_MODULE_ENABLED
5.1

## Slide 17: Use BSP for LCD init and writing
BSP LCD organization
BSP package
Our project
Discovery drivers
HAL API
Components
stm32f4xx_discovery.c
stm32f4xx_discovery_lcd.c
stm32f4xx_discovery_sdram.c
ili9341.c
lis3dsh.c
stmpe811.c
stm32f4xx_II_fmc.c
stm32f4xx_hal_ltdc.c
stm32f4xx_hal_spi.c
stm32f4xx_hal_i2c.c
stm32f4xx_hal.c
stm32f4xx_hal_sdram.c
Utilities
Fonts
5.2

## Slide 18: Use BSP for LCD init and writing
BSP LCD organization
BSP package
Our project
Discovery drivers
HAL API
Components
stm32f4xx_discovery.c
stm32f4xx_discovery_lcd.c
stm32f4xx_discovery_sdram.c
ili9341.c
lis3dsh.c
stmpe811.c
stm32f4xx_II_fmc.c
stm32f4xx_hal_ltdc.c
stm32f4xx_hal_spi.c
stm32f4xx_hal_i2c.c
stm32f4xx_hal.c
1. include stm32f4xx_discovery_lcd.h
stm32f4xx_hal_sdram.c
Utilities
Fonts
2. stm32f4xx_discovery_lcd.h use the discovery BSP and SDRAM
5.2

## Slide 19: Use BSP for LCD init and writing
BSP LCD organization
BSP package
Our project
Discovery drivers
HAL API
Components
stm32f4xx_discovery.c
stm32f4xx_discovery_lcd.c
stm32f4xx_discovery_sdram.c
ili9341.c
lis3dsh.c
stmpe811.c
stm32f4xx_II_fmc.c
stm32f4xx_hal_ltdc.c
stm32f4xx_hal_spi.c
stm32f4xx_hal_i2c.c
stm32f4xx_hal.c
3. stm32f4xx_discovery_lcd.h use driver ili9341.c which is TFT LCD controller
stm32f4xx_hal_sdram.c
Utilities
Fonts
4. stm32f4xx_discovery_lcd.h use LCTD controller from HAL
5.2

## Slide 20: Use BSP for LCD init and writing
BSP LCD organization
BSP package
Our project
Discovery drivers
HAL API
Components
stm32f4xx_discovery.c
stm32f4xx_discovery_lcd.c
stm32f4xx_discovery_sdram.c
ili9341.c
lis3dsh.c
stmpe811.c
stm32f4xx_II_fmc.c
stm32f4xx_hal_ltdc.c
stm32f4xx_hal_spi.c
stm32f4xx_hal_i2c.c
stm32f4xx_hal.c
stm32f4xx_hal_sdram.c
Utilities
Fonts
2. stm32f4xx_discovery_lcd.h use fonts from utility folder
5.2

## Slide 21: Use BSP for LCD init and writing
We use the project from BSP SDRAM because the LCD also use the SDRAM
We need copy the Fonts from Utilities folder in CubeMX repository
5.2

## Slide 22: Use BSP for LCD init and writing
The copy part
  In our project in Drivers folder create folder Utilities
  Now go into CubeMX repository …\STM32Cube_FW_F4_V1.3.0\Utilities\
  And copy Fonts into Utilities folder
Copy folders into Utilities
5.2

## Slide 23: Use BSP for LCD init and writing
We add the driver for LCD from HAL
Right click on STM32F4xx_HAL_Drive>ADD from \Drivers\STM32F4xx_HAL_Driver\Src
  stm32f4xx_hal_ltdc.c
  Stm32f4xx_hal_dma2d.c
5.2

## Slide 24: Use BSP for LCD init and writing
We add the driver for BSP LDC
Right click on BSP>ADD from \Drivers\BSP\STM32F429I-Discovery\
  stm32f429i_discovery_lcd.c
Right click on BSP>ADD from \Drivers\BSP\Components\ili9341\
  ili9341.c
5.2

## Slide 25: Use BSP for LCD init and writing
Now last thing is allow to include new HAL files which we added
  Open stm32f4xx_hal_conf.h in ..\Inc\
  Uncomment files which we added
  HAL_DMA2D_MODULE_ENABLED
  HAL_LTDC_MODULE_ENABLED
5.2

## Slide 26: Use BSP for LCD init and writing
Into main.c now we modify include from stm32f429i_discovery_sdram.h to stm32f429i_discovery_lcd.h
And remove the BSP_SDRAM_Init()
/* USER CODE BEGIN Includes */
#include "stm32f429i_discovery_lcd.h"
/* USER CODE END Includes */
/* USER CODE BEGIN 2 */
/* USER CODE END 2 */
5.2

## Slide 27: Use BSP for LCD init and writing
Simple LCD demonstration
/* USER CODE BEGIN 2 */
BSP_LCD_Init();//init LCD
//set the layer buffer address into SDRAM
BSP_LCD_LayerDefaultInit(1, SDRAM_DEVICE_ADDR);
BSP_LCD_SelectLayer(1);//select on which layer we write
BSP_LCD_DisplayOn();//turn on LCD
BSP_LCD_Clear(LCD_COLOR_BLUE);//clear the LCD on blue color
BSP_LCD_SetBackColor(LCD_COLOR_BLUE);//set text background color
BSP_LCD_SetTextColor(LCD_COLOR_WHITE);//set text color
//write text
BSP_LCD_DisplayStringAtLine(2,"Cube STM32");
BSP_LCD_DisplayStringAtLine(3,"BSP");
BSP_LCD_DisplayStringAtLine(4,"LCD DEMO");
/* USER CODE END 2 */
5.2

## Slide 28: 5.3 BSP EEPROM lab

## Slide 29: Use BSP to access EEPROM
Objective
  Learn how import BSP EEPROM into project
  We use the project from lab 26
  Which part need to by configured in GUI
  Try to write text into EEPROM and read it
  Read text from EEPROM and display it on LCD
Goal
  Successfully import BSP EEPROM drivers into your project
  Learn which part you need to import
  How to setup the project
5.3

## Slide 30: Use BSP to access EEPROM
BSP EEPROM organization
BSP package
Our project
Discovery drivers
HAL API
Components
stm32f4xx_discovery.c
stm32f4xx_discovery_lcd.c
stm32f4xx_discovery_sdram.c
ili9341.c
lis3dsh.c
stmpe811.c
stm32f4xx_II_fmc.c
stm32f4xx_hal_ltdc.c
stm32f4xx_hal_spi.c
stm32f4xx_hal_i2c.c
stm32f4xx_hal.c
stm32f4xx_hal_sdram.c
Utilities
Fonts
stm32f4xx_discovery_io.c
stm32f4xx_discovery_eeprom.c
5.3

## Slide 31: Use BSP to access EEPROM
BSP EEPROM organization
BSP package
Our project
Discovery drivers
HAL API
Components
stm32f4xx_discovery.c
stm32f4xx_discovery_lcd.c
stm32f4xx_discovery_sdram.c
ili9341.c
lis3dsh.c
stmpe811.c
stm32f4xx_II_fmc.c
stm32f4xx_hal_ltdc.c
stm32f4xx_hal_spi.c
stm32f4xx_hal_i2c.c
stm32f4xx_hal.c
stm32f4xx_hal_sdram.c
Utilities
Fonts
stm32f4xx_discovery_io.c
stm32f4xx_discovery_eeprom.c
1. Use functions from stm32f4xx_discovery_eeprom.c
5.3

## Slide 32: Use BSP to access EEPROM
BSP SDRAM organization
BSP package
Our project
Discovery drivers
HAL API
Components
stm32f4xx_discovery.c
stm32f4xx_discovery_lcd.c
stm32f4xx_discovery_sdram.c
ili9341.c
lis3dsh.c
stmpe811.c
stm32f4xx_II_fmc.c
stm32f4xx_hal_ltdc.c
stm32f4xx_hal_spi.c
stm32f4xx_hal_i2c.c
stm32f4xx_hal.c
stm32f4xx_hal_sdram.c
Utilities
Fonts
stm32f4xx_discovery_io.c
stm32f4xx_discovery_eeprom.c
2. stm32f4xx_discovery_eeprom.c call functions from stm32f4xx_discovery_io.c
3. stm32f4xx_discovery_io.c call functions from stm32f4xx_discovery.c
pin init and write/read functions
5.3

## Slide 33: Use BSP to access EEPROM
BSP EEPROM organization
BSP package
Our project
Discovery drivers
HAL API
Components
stm32f4xx_discovery.c
stm32f4xx_discovery_lcd.c
stm32f4xx_discovery_sdram.c
ili9341.c
lis3dsh.c
stmpe811.c
stm32f4xx_II_fmc.c
stm32f4xx_hal_ltdc.c
stm32f4xx_hal_spi.c
stm32f4xx_hal_i2c.c
stm32f4xx_hal.c
stm32f4xx_hal_sdram.c
Utilities
Fonts
stm32f4xx_discovery_io.c
stm32f4xx_discovery_eeprom.c
4. stm32f4xx_discovery.c
Use stm32f4xx_hal_i2c to commutate with eeprom memory
5.3

## Slide 34: Use BSP to access EEPROM
We use the project from BSP LCD lab 26 because we want to display the memory content on LCD
5.3

## Slide 35: Use BSP to access EEPROM
We add the driver for BSP LDC
Right click on BSP>ADD from \Drivers\BSP\STM32F429I-Discovery\
  stm32f429i_discovery_eeprom.c
  stm32f429i_discovery_io.c
5.3

## Slide 36: Use BSP to access EEPROM
Add the define of EEPROM into project options
  Right click on project>Options>Category C/C++Compiler>Preprocesor
  Into Defined symbols add EE_M24LR64
  This allow use EEPROM functions
  Button OK close project options
5.3

## Slide 37: Use BSP to access EEPROM
Use the ATM7-M24LR-A board with M24LR memory and connect it into STM32F429i-Discovery kit
5.3

## Slide 38: Use BSP to access EEPROM
Into main.c now modify include
Define variables
/* USER CODE BEGIN Includes */
#include "stm32f429i_discovery_lcd.h"
#include "stm32f429i_discovery_io.h"
#include "stm32f429i_discovery_eeprom.h"
#include <string.h>
/* USER CODE END Includes */
/* USER CODE BEGIN PV */
uint8_t text_to_write[]="test text";//write to eeprom
uint8_t text_to_read[200];//read from eeprom
uint32_t address=0;//address in eeprom
uint16_t read_num=1;//number of bytes which we want to read from eeprom
/* USER CODE END PV */
5.3

## Slide 39: Use BSP to access EEPROM
Into stm32f4xx_it.c add global variable for i2c handle
and define handler functions for I2C DMA
/* USER CODE BEGIN 0 */
extern I2C_HandleTypeDef I2cHandle;
/* USER CODE END 0 */
/* USER CODE BEGIN 1 */
void DMA1_Stream4_IRQHandler()
{
HAL_DMA_IRQHandler(I2cHandle.hdmatx);
}
void DMA1_Stream2_IRQHandler()
{
HAL_DMA_IRQHandler(I2cHandle.hdmarx);
}
/* USER CODE END 1 */
5.3

## Slide 40: Use BSP to access EEPROM
Into main.c add
/* USER CODE BEGIN 2 */
/*LCD init*/
BSP_LCD_Init();
BSP_LCD_LayerDefaultInit(1, SDRAM_DEVICE_ADDR);
BSP_LCD_SelectLayer(1);
BSP_LCD_DisplayOn();
BSP_LCD_Clear(LCD_COLOR_BLUE);
BSP_LCD_SetBackColor(LCD_COLOR_BLUE);
BSP_LCD_SetTextColor(LCD_COLOR_WHITE);
/*EEPROM init*/
BSP_EEPROM_Init();
/*Write text into EEPROM*/
BSP_EEPROM_WriteBuffer(text_to_write,0,(strlen(text_to_write)+1));
/*Read text from EEPROM*/
do{
BSP_EEPROM_ReadBuffer((uint8_t*)&(text_to_read[address]),address,(uint16_t*)&read_num);
}while(text_to_read[address++]!=0x0);
/*Display text*/
BSP_LCD_DisplayStringAtLine(2,text_to_read);
/* USER CODE END 2 */
5.3

## Slide 41: 5.4 BSP GYRO lab

## Slide 42: Use BSP to access GYROSCOPE
Objective
  Learn how import BSP GYROSCOPE into project
  We use the project from lab 26
  Which part need to by configured in GUI
  Read data from GYROSCOPE and display it on LCD
Goal
  Successfully import BSP GYROSCOPE drivers into your project
  Learn which part you need to import
  How to setup the project
5.4

## Slide 43: Use BSP to access GYROSCOPE
BSP GYRO organization
BSP package
Our project
Discovery drivers
HAL API
Components
stm32f4xx_discovery.c
stm32f4xx_discovery_lcd.c
stm32f4xx_discovery_sdram.c
ili9341.c
lis3dsh.c
stmpe811.c
stm32f4xx_II_fmc.c
stm32f4xx_hal_ltdc.c
stm32f4xx_hal_spi.c
stm32f4xx_hal_i2c.c
stm32f4xx_hal.c
stm32f4xx_hal_sdram.c
Utilities
Fonts
stm32f4xx_discovery_io.c
stm32f4xx_discovery_gyroscope.c
5.4

## Slide 44: Use BSP to access GYROSCOPE
BSP GYRO organization
BSP package
Our project
Discovery drivers
HAL API
Components
stm32f4xx_discovery.c
stm32f4xx_discovery_lcd.c
stm32f4xx_discovery_sdram.c
ili9341.c
lis3dsh.c
stmpe811.c
stm32f4xx_II_fmc.c
stm32f4xx_hal_ltdc.c
stm32f4xx_hal_spi.c
stm32f4xx_hal_i2c.c
stm32f4xx_hal.c
stm32f4xx_hal_sdram.c
Utilities
Fonts
stm32f4xx_discovery_io.c
stm32f4xx_discovery_gyroscope.c
1. Use functions from stm32f4xx_discovery_eeprom.c
5.4

## Slide 45: Use BSP to access GYROSCOPE
BSP GYRO organization
BSP package
Our project
Discovery drivers
HAL API
Components
stm32f4xx_discovery.c
stm32f4xx_discovery_lcd.c
stm32f4xx_discovery_sdram.c
ili9341.c
lis3dsh.c
stmpe811.c
stm32f4xx_II_fmc.c
stm32f4xx_hal_ltdc.c
stm32f4xx_hal_spi.c
stm32f4xx_hal_i2c.c
stm32f4xx_hal.c
stm32f4xx_hal_sdram.c
Utilities
Fonts
stm32f4xx_discovery_io.c
stm32f4xx_discovery_gyroscope.c
2. stm32f4xx_discovery_gyroscope.c call functions from stm32f4xx_discovery_io.c
3. stm32f4xx_discovery_io.c call functions from stm32f4xx_discovery.c
pin init and read functions
5.4

## Slide 46: Use BSP to access GYROSCOPE
BSP GYRO organization
BSP package
Our project
Discovery drivers
HAL API
Components
stm32f4xx_discovery.c
stm32f4xx_discovery_lcd.c
stm32f4xx_discovery_sdram.c
ili9341.c
lis3dsh.c
stmpe811.c
stm32f4xx_II_fmc.c
stm32f4xx_hal_ltdc.c
stm32f4xx_hal_spi.c
stm32f4xx_hal_i2c.c
stm32f4xx_hal.c
stm32f4xx_hal_sdram.c
Utilities
Fonts
stm32f4xx_discovery_io.c
stm32f4xx_discovery_gyroscope.c
4. stm32f4xx_discovery.c
Use stm32f4xx_hal_spi to commutate with gyroscope
5.4

## Slide 47: Use BSP to access GYROSCOPE
We use the project from BSP LCD lab 26 because we want to display gyro values on LCD
5.4

## Slide 48: Use BSP to access GYROSCOPE
We add the driver for BSP LDC
Right click on BSP>ADD from \Drivers\BSP\STM32F429I-Discovery\
  stm32f429i_discovery_gyroscope.c
  stm32f429i_discovery_io.c
Right click on BSP>ADD from \Drivers\BSP\Components\
  l3gd20.c
5.4

## Slide 49: Use BSP to access GYROSCOPE
Into main.c now modify include
Define variables
/* USER CODE BEGIN Includes */
#include "stm32f429i_discovery_lcd.h"
#include "stm32f429i_discovery_gyroscope.h"
#include "stm32f429i_discovery_io.h"
#include <stdio.h>
/* USER CODE END Includes */
/* USER CODE BEGIN PV */
float valxyz[3];//gyroscope values
uint8_t buffer[200];//text buffer
/* USER CODE END PV */
5.4

## Slide 50: Use BSP to access GYROSCOPE
Into main.c add
/* USER CODE BEGIN 2 */
/*LCD init*/
BSP_LCD_Init();
BSP_LCD_LayerDefaultInit(1, SDRAM_DEVICE_ADDR);
BSP_LCD_SelectLayer(1);
BSP_LCD_DisplayOn();
BSP_LCD_Clear(LCD_COLOR_BLUE);
BSP_LCD_SetBackColor(LCD_COLOR_BLUE);
BSP_LCD_SetTextColor(LCD_COLOR_WHITE);
/*Gyroscope init*/
BSP_GYRO_Init();
/* USER CODE END 2 */
5.4

## Slide 51: Use BSP to access GYROSCOPE
Into main.c add
/* USER CODE BEGIN 3 */
/* Infinite loop */
while (1)
{
/*Get Gyrospope value*/
BSP_GYRO_GetXYZ(valxyz);
/*Display X*/
sprintf(buffer,"x:%f",valxyz[0]);
BSP_LCD_DisplayStringAtLine(2,buffer);
/*Display Y*/
sprintf(buffer,"y:%f",valxyz[1]);
BSP_LCD_DisplayStringAtLine(3,buffer);
/*Display Z*/
sprintf(buffer,"z:%f",valxyz[2]);
BSP_LCD_DisplayStringAtLine(4,buffer);
/*Delay*/
HAL_Delay(1000);
}
/* USER CODE END 3 */
5.4

## Slide 52: www.st.com/stm32